## Slide 1
New EM210_AV

## Slide 2
EM210 – Housing
No difference!
EM21=EM210

## Slide 3
EM210_AV – New features
  Measurement on three-phase systems without neutral (always self-power supply)
EM21_AV
Mandatory connection!
(supply between L1 and N)
EM210_AV
Neutral not required
(supply between L2 and L3)
Notes: Aggiunte features

## Slide 4
  High serial communication speed
  Selectable parity mode and selectable stop bit
EM21_AV
9.6 kbps
No parity
1 stop bit
EM210_AV
9.6 - 19.2 - 38.4 - 57.6 - 115.2 kbps
None or even parity
1 or 2 stop bit
EM210_AV – New features
Notes: Aggiunte features

## Slide 5
  New protocol compatible with all other coming CG meters
EM210_AV – New features
Notes: Aggiunte features

## Slide 6
  Exported (negative) kWh meter in new E application; new F application too
EM21_AV
EM210_AV – New features
Notes: Aggiunte features

## Slide 7
  Voltages and currents THD measurements, current neutral (calculated), working hours
EM210_AV – New features
Notes: Aggiunte features

## Slide 8
  Wrong connection function (available over communication port) (1/2)
  Enabling, disabling
  Detection of wrong voltage phase sequence
  Detection of wrong association between phase voltage and phase current
  Detection of wrong secondary current connection
EM210_AV – New features
Notes: Aggiunte features

## Slide 9
  Wrong connection function (available over communication port) (2/2)
    The algorithm works with loads whose PF
    is between 0.77L and 0.99C
EM210_AV – New features
Notes: Aggiunte features

## Slide 10
  Selectable pulse duration
TOFF ≥ 120 ms
(according to EN62052-31)
TON selectable: 30 ms or 100 ms
(according to EN62052-31)
Opto-mosfet output
(linked to +kWh)
EM210_AV – New features
Notes: Aggiunte features

## Slide 11
  New terminals position for better error-proof connection
I1 I2 I3 (N L)
In Out In Out In Out N L1 L2 L3
EM210_AV
EM21_AV
EM210_AV
EM210_AV – New features
Notes: Aggiunte features

## Slide 12
EM210_AV – Main features
External current transformer connection (5A)
Full set of variables available to perform a complete load analysis
Energy measurement kWh (total imported active energy, total exported active energy) and total reactive energy for an accurate cost allocation
Easy connections management
One digital outputs and RS485 communication port for quick and easy data transmission to PC/PLC for full load control or integration to BMS
Detachable display
Multi-use housing: for both DIN-rail and panel mounting applications
Power supply: self power supply from 40V to 480VAC (connection VL2-L3)

## Slide 13
Key Specifications
Housing (H x W x D): 72x72x64.6 mm
Display type: LCD, 2 lines: 1st line:7-DGT, 2nd line:3-DGT + 3-DGT
Instantaneous variables: 3 x 3 DGT
Energy variables: 1x 5+2DGT, 6+1DGT, 7 DGT
Accuracy: W-VA-PF: ±(1% RDG+2DGT); var: ±(2% RDG+2DGT);
V LN-A: ±(0.5% RDG+1DGT), kWh: Class B (EN50470-3), Class1 (EN62053-21);
kvarh: Class 2 (EN62053-23).
System type: Unbalanced: 2-3-phase; 1-phase
Voltage inputs (Un): 120/230VLLAC (AV6 model)
400VLLAC (AV5 model)
Current inputs (In): In: 5AAC, Imax: 6AAC (shunt input technology)
Method: TRMS
Digital Pulse Output: Proportionate to measured active energy (EN62052-31)
Serial Communication Port: RS485 (2-wire, Modbus), RTU protocol (Baud-rate 9.6, 19.2, 38.4, 57.6, 115.2 kbps)
Power supply: Self power supply (from 40V to 480VAC through terminals VL2-L3)
Temperature range: operating: -25°C to +55°C;
storage: -30°C to +70°C
Approvals: CE, cULus listed
Protection degree: IP50 (front)
EM210_AV – Main features

## Slide 14
EM210_AV – Wiring
LOAD
1
2
3
4
5
6
Neutral
Phase 1
Phase 2
Phase 3
The use of external
current transformers
is mandatory

## Slide 15
3-phase + N unbalance sys
(3 CT connection)
3-phase + N unbalance sys
(3-CT + 3-VT connection)
3-phase without N unbalance sys
(3-CT connection)
3-phase without N unbalance sys
(3-CT + 3-VT connection)
2-phase + N unbalance sys
(2-CT connection)
2-phase + N unbalance sys
(2-CT + 2-VT connection)
L1
L2
New
EM210_AV – Wiring

## Slide 16
EM210_AV – Applications
New